## Slide 1: Single Catchment Delineation using ArcGIS
Vijay Singh Meena,
Deputy Director
Central Water Commission

## Slide 2: Catchment Parameter Estimation using Arc GIS
To calculate:
1 Catchment Area
2 Longest flow Path
3 Centroidal Length
4 Slope

## Slide 3: Selection of SRTM File
LATITUDE | 
5 - 10 N | _11
10 - 15 N | _10
15 - 20 N | _09
20 - 25 N | _08
25 - 30 N | _07
30 - 35 N | _06
LONGITUDE | 
60 - 65 E | 49
65 - 70 E | 50
70 - 75 E | 51
75 - 80 E | 52
80 - 85 E | 53
85 - 90 E | 54
90 - 95 E | 55
95 - 100 E | 56
Project Location:
Longitude 76° 42’ 23.10” E
Latitude 10° 13’ 18.85” N

## Slide 4: Selection of SRTM File
E.g. Idamalayar Dam
Project location is 76° 42’ 23.10” E and 10° 13’ 18.85” N
Longitude is between 75 E to 80 E
Latitude is between 10 N to 15 N
So SRTM File to be used is 52_10

## Slide 5: Make a Project folder
Let’s Start !!!
Make the project folder and paste relevant SRTM file in it.
Connect this SRTM File and assign it proper coordinate system as described in next steps.

## Slide 6: Catalog to Connect to Folder
Arc GIS interface

## Slide 7: Adding the Project Folder
Using

## Slide 8: Folder Connection Step
Select the folder created for the project

## Slide 9: Connect to Projects SRTM File (Data Management Tools->Projection & Transformations->Raster->Project Raster
Provide projection to the SRTM file

## Slide 10: Add OUTPUT COORDINATE SYSTEM
Longitude/ Easting | UTM Zones
60 - 66 E | 41 N
66 - 72 E | 42 N
72 - 78 E | 43 N
78 - 84 E | 44 N
84 - 90 E | 45 N
90 - 96 E | 46 N
Select UTM zone Using the Table below

## Slide 11: Check Coordinate System(Right Click->Data Frame Properties)
Check whether SRTM projected or not.
Rt. Click Data Frame Property Coordinate System

## Slide 12
Check whether coordinate system assigned successfully, if not reassign the same
Save the work with relevant project name

## Slide 13: Perform the PREPROCESSING STEPS ( Fill Sinks to Adjoint Catchment Processing)-Fill sink
A sink is a cell with an undefined drainage direction; no cells surrounding it are lower.

## Slide 14
Fill Sink completed
After Completion of Fill sink step, DEM color changes as shown

## Slide 15
Flow Direction computations
The D8 flow method models flow direction from each cell to its steepest downslope neighbor.

## Slide 16
Flow Accumulation computations
The result of Flow Accumulation is a raster of accumulated flow to each cell, as determined by accumulating the weight for all cells that flow into each downslope cell.

## Slide 17
Flow Accumulation computations

## Slide 18
Stream definition
In this step we provide condition (Area or No. of cells contributing) to define a stream.

## Slide 19
Stream definition completed

## Slide 20
Stream segmentaion
Assigns unique values to sections of a raster linear network between intersections.

## Slide 21
Catchment Grid Delineation
In this step area contributing each Stream Segment is estimated

## Slide 22
Catchment Grid Delineation contd....

## Slide 23
Catchment Polygon processing
Catchment Grids generated above are converted from Raster to Vector

## Slide 24: Drainage line processing
Stream Links generated are converted to Vector

## Slide 25: Adjoint catchment processing
Adjoint small catchments club together

## Slide 26: To Start New Project
Preprocessing steps completed and project specific steps started here after

## Slide 27: Start New Project
Check whether the project point lies inside the DEM or not using XY tool.

## Slide 28: Define the project
Name your project

## Slide 29: Start New Project

## Slide 30: Now add project point (Locate the project location using ‘’GO TO XY’’, See next slides to locate the project point)

## Slide 31: Go to XY and locate project

## Slide 32: Add project coordinates(23°32’55.54” N & 85°08’3.93” E) and flash to locate the project point

## Slide 33: Zoom near Project Point to mark the project Point

## Slide 34: Project Points
Mark the project point on the stream, failing which catchment not delineated

## Slide 35: Generate Project

## Slide 36: Catchment processing contd.......

## Slide 37: Delineated catchment

## Slide 38: Basin Merge
Using select feature tool (Shown below) select whole catchment for basin merge

## Slide 39: Basin Merge contd....
After selecting the basins, it looks like this.

## Slide 40: Merged Basin

## Slide 41: Go to Characteristics : perform River Length, River Slope, Longest Flow path, Basin Centroid, Centroidal Longest Flow path etc one by one.

## Slide 42: River length computation

## Slide 43: River slope computation

## Slide 44: Longest flow path computation

## Slide 45: Basin centroid computation

## Slide 46: Centroid elevation computation

## Slide 47: Centroidal longest flow path

## Slide 48: Estimation of River Length, Basin Centroid, Longest River Path, Basin Centroid, Centroidal Longest Flow Path
After completion the above steps, to check the estimated lengths, we right click and open Attribute table

## Slide 49: Seeing values from attribute table

## Slide 50: Calculation of Slope

## Slide 51: River Slope Profile
We careful in this step, while selecting Line2Profile Option.

## Slide 52: Computation of Equivalent Slope
EQUIVALENT SLOPE |  |  |  |  | 
Chainage (km) | Reduced Level (m) | Height above Datum Di (m) | Length of each segment Li (km) | (Di+Di-1)Li (km.m) | 
59.6 | 120 | 0 | 0 | 0 | 
45 | 156 | 36 | 14.6 | 525.6 | 
40 | 207 | 87 | 5 | 1705.2 | 
35 | 436 | 316 | 5 | 3160 | 
34 | 553 | 433 | 1 | 2598 | 
30 | 576 | 456 | 4 | 2280 | 
27 | 613 | 493 | 3 | 3451 | 
25 | 775 | 655 | 2 | 3275 | 
23 | 983 | 863 | 2 | 3452 | 
20 | 1032 | 912 | 3 | 4560 | 
15 | 1161 | 1041 | 5 | 8328 | 
14 | 1236 | 1116 | 1 | 6696 | 
12 | 1589 | 1469 | 2 | 4407 | 
10 | 1690 | 1570 | 2 | 6280 | 
5 | 1879 | 1759 | 5 | 12313 | 
0 | 2488 | 2368 | 5 | 23680 | 
Longest River Length from outlet (L) |  |  | 59.6 |  | 
Ʃ{(Di+Di-1)Li} |  |  |  | 86710.80 | 
Equivalent stream slope Ʃ{(Di+Di-1)Li}/L2 |  |  | Seq | 24.41 | m /km

## Slide 53: Catchment Area Delineation (ArcGIS)
CA | 472 | sq. km
L | 59.6 | km
Lc | 26.2 | km
ESS | 24.41 | m/km

## Slide 54
Thank You !
धन्यवाद !